## Slide 1
S T A C W A R S · P S 4
Mining the Asteroid Belt
BENNU WELL
“Forget platinum, Han. Water is the real treasure.”
Founding team pitch for Han Solo & Chewbacca
IIT Mandi · Team: Beyond Infinity
Turning Asteroid Resources into a Water Supply for Spaceurnig

## Slide 2
SUBPART A · ENGINEERING · 1 / 2
Target Bennu, mine water, sell it near the Moon
Subpart A: how the ship gets there, what it mines, where the cargo goes
Per trip (our model): 316 t mined, 116 t burned on the way home, 185 t sold. Bennu water content from OSIRIS-REx hydrogen map (0.71 wt% H).
1
EARTH
LEO
Moon
WATER DEPOT
NRHO / L2: customers here
BENNU
1 Starship drops tug in LEO
2 Spiral out on water thrusters (~1 yr)
3 Hover, anchor, mine ~300 days
4 Home on Bennu water (~1 yr)
5 Sell, refuel, repeat
Outbound 2 km/s, return 1-2 km/s (assumed, tug is light and Bennu gravity is tiny)
Why Bennu
490 m rubble pile, so almost no gravity to fight when leaving.
Samples are over 80 vol% water-bearing clay; hydrogen map gives about 6 wt% water-equivalent. We plan on 5.
3.7 million tones of water at 5%. We need 5.5 thousand.
Ryugu was our first guess but its samples are almost dry (<0.3 wt% interlayer water). Dropped.
Honest catch: Bennu is on the hazardous-asteroid list. We remove a tiny fraction of its mass, but expect regulators to ask.
Notes: Route and target. Bennu chosen because returned samples are mostly hydrated clay; hydrogen 0.71 wt% maps to roughly 6 wt% water-equivalent, we plan on 5. Delta-v values are our assumptions.

## Slide 3
SUBPART A · ENGINEERING · 2 / 2
The rig: let sunlight do the digging
Subpart A: extraction tool, processing, power, and what happens when it breaks
Concept basis: optical mining (NASA NIAC / TransAstra) and a steam-hopper prototype with 87% water recovery in lab. Scale-up to 316 t per trip is our assumption.
2
Bennu surface: hydrated clay boulders
capture bag
+ rubble, sealed
thin-film solar concentrators
SUN
cold plate
condenser
water tank
(200 t)
anchor harpoons
Reach + land
Tug hovers with optical nav + LIDAR, fires harpoons to hold on. No landing, no wheels.
Extract
Bag swallows a patch; mirrors heat it to ~500 C; clay releases water vapour.
Process
Vapour freezes on a cold plate, melts into the tank. Dry rock is dumped (or kept as shielding bulk).
Use + energy
Water stays in space as propellant and life-support water. Power is solar only, ~70 kW thermal at the oven.
Breaks anyway
Two tugs per base, spare bags, hover-and-wait safe mode. Ground sets goals; onboard autonomy runs the loops since signals take minutes.
Never tell me the odds. Bottleneck: capturing and baking loose rubble in microgravity at scale. Assumed breakthrough: optical mining proven in orbit, plus ~500 s water thrusters.
Notes: Optical mining concept (NIAC / TransAstra) and the Honeybee steam-hopper test (87% recovery). Energy 5.8 MJ/kg water with 50% heat recovery. Thruster Isp 500 s is an assumption.

## Slide 4
SUBPART B · COST · 1 / 2
Where the money goes, and how we shrink it
Subpart B: three biggest cost drivers, our fixes, and what we have to assume
Total CAPEX $1711M including 20% contingency; opex $395M over 20 years. Launch price: contract seen at $90M, we assume $60M as flights get routine.
3
Chart: CAPEX by item ($M, with contingency)
| Launch $576M | Tug fleet $506M | Mining bases $389M | Development $240M
CAPEX | 576 | 506 | 389 | 240
Assumptions we are making
Starship: 150 t to LEO, $60M/flight, one flight per tug. Tug: 30 t dry, 200 t cargo, 500 s thruster, 2.5 yr round trip. Tug cost falls 15% per doubling. 10% discount rate.
1
Launch to orbit 34% of CAPEX
Fly once per tug, never launch propellant again. After the first fill the ships drink Bennu water.
Tech we assume: Reusable Starship at ~$60M/flight
2
Tug fleet 30% of CAPEX
One design built six times, so unit cost drops. Each tug flies about 8 trips.
Tech we assume: 15% learning curve, 20 yr hardware life
3
Mining bases 23% of CAPEX
Replace drills, diggers and crushers with a bag and mirrors.
Tech we assume: Optical mining works at flight scale
Notes: CAPEX split from our model. Launch $60M per flight is an assumption, a $90M contract has been reported. Learning curve 85%.

## Slide 5
SUBPART B · COST · 2 / 2
Why Mine Water in Space Instead of Carrying It?
Subpart B bonus: comparison with conventional asteroid mining, plus what breaks our numbers
Earth baselines are our own estimates (Falcon 9 ~$3,000/kg to LEO or Starship ~$600/kg, times ~3.3 mass penalty to lunar orbit). Conventional column is qualitative.
4
 | Conventional plan | Bennu Well
Product | Platinum-group metals sent to Earth | Water, kept in space
Propellant | Launched from Earth, e.g. xenon, every mission | Mined on site, $0 after first fill
Trip home | Re-entry capsule, tiny cargo, one-off | Reusable tug, 185 t sold per trip
Mining kit | Drills, crushers, ore handling | Inflatable bag + mirrors
Cost per kg | Metal must beat Earth mines at home | ~$380/kg water vs $2,000-10,000 from Earth
Chart: Project IRR when one thing goes wrong
| Base case | Price $2,000/kg | Launch $90M | 2-yr delay | Price $700/kg | Hardware cost x2 | Water yield -50%
IRR % | 14.1 | 26.1 | 12.2 | 10.8 | 8.7 | 8.5 | 3.8
Yield is the soft spot: if the rig recovers half the water we plan for, IRR falls to 3.8%. Price and hardware cost matter next. Launch cost barely moves it.
Why it is cheaper: we never pay to haul propellant up a gravity well, and the cargo is bulk water that sells where it is made.
Notes: Conventional comparison is qualitative. IRR sensitivities come straight from the cost model. Earth baseline $/kg are our estimates.

## Slide 6
SUBPART C · BUSINESS · 1 / 2
Who pays for water, and where we sell it
Subpart C: product, customers with assumptions, where to sell, how we earn
ULA publicly bid $1,000/kg for propellant in lunar orbit and $3,000-7,000/kg in LEO (IAC-18 paper). Demand figure on this slide is our assumption, not a signed order.
5
Customer | What they use water for | Where we stand
Satellite refuelling + tug operators (Orbit Fab, Astroscale, Space Force programs) | Propellant top-ups, water thrusters | Demos flying 2026
Launch companies building depots | Stage propellant in cislunar space | Public price bid
Space stations and lunar missions | Crew water, shielding, landers | Prospect only
Demand assumption: cislunar users need at least 400 t of water a year by the mid-2030s. We sell about 370.
A Bring to Earth
No. Re-entry costs, and Earth water is nearly free.
B Use it ourselves
Yes. 116 t per trip is our own return fuel.
C Sell in cislunar space
Yes. This is the revenue line.
How we make money
$1,000
per kg of water delivered to the depot
~$370M
revenue a year once 6 tugs run (about 370 t sold)
Take-or-pay contracts signed before launch, so lenders see the cash.
Dried clay left over can be sold as radiation-shielding bulk (not counted in our numbers).
Notes: Customers: Orbit Fab, Astroscale, Space Force refuelling demos; ULA public bid $1,000/kg lunar orbit. Demand of 400 t/yr is our assumption.

## Slide 7
SUBPART C · BUSINESS · 2 / 2
Does Han get paid? And what could sink us
Subpart C: the numbers, then the bad feelings
Model: 6 tugs, 2 mining bases, 20-year horizon, 10% discount rate, 20% contingency. Break-even is when cumulative cash turns positive.
6
Chart: Cumulative cash by year ($M)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Cumulative cash ($M) | -80 | -160 | -402 | -774 | -954 | -1126 | -1109 | -1090 | -1093 | -745 | -398 | 134 | 480 | 1010 | 1355 | 1700 | 2229 | 2572 | 3099 | 3441
Yr 11
break-even
$1.7B
CAPEX
$1126M
peak funding
$395M
NPV at 10%
14.1%
IRR
Roadmap: yr 0-2 ground tests + offtake letters > yr 3 pilot tug launches > yr 6 first sale > yr 8-11 fleet of six, break-even
Nobody buys yet
Cislunar demand is thin today. We sign take-or-pay letters before the first launch and start with one pilot tug, so a miss costs a pilot, not the fleet.
Cheaper water appears
Cheaper Starship or lunar ice could push the price down. NPV stays positive down to about $770/kg and our cost is $380/kg.
The rig underperforms
If yield halves, IRR falls to 3.8%. So funding is staged: no fleet money until the pilot proves the yield.
Regulators and Bennu
It is a hazardous-asteroid listing. Share tracking data openly and partner with an agency.
Notes: Cash: 8 Starship launches, 6 tugs, 2 bases. Break-even year 11, NPV $395M at 10%, IRR 14.1%.

## Slide 8
Thank you
Han, here are the odds: 14.1% IRR, break-even in year 11, water at $380/kg.